## Slide 1: Entwicklung einer Digital Twin-Applikation für einen Industrieroboter mit ROS und OPC-UA
Ahmed Ibrahim Almohamed
ibraah03@thu.de

## Slide 2: Agenda
Project definition
Technical Foundations
System Architecture
System Workflow
Use Case (Virtual Commissioning)
Areas for Improvement

## Slide 3: Project Definition
Connection of the Kuka KR3 to ROS2
Specification of an integrated ROS controller for a robot cell
Further development of the ROS laboratory test for physical Kuka KR3
Analyzing application scenarios for digital twins and industrial robots
Implementation of a DT application

## Slide 4: Technical Foundations
Digital Twin
Notes: What is a DT ?
represents the creation of a virtual replica of a physical object or system that is used to simulate, monitor, and optimize its real-world counterpart.

## Slide 5: Technical Foundations
Level of Integration
Notes: Layers of integration :
Mirroring or Digital Model : Digital representation of a physical entity
Digital Shadow : Physical to virtual uni-directional information flow
Digital Twin : virtual to physical bi-directional information flow

## Slide 6: Technical Foundations
ROS2 Nodes
Notes: ROS2 Nodes :
A node is a participant in the ROS 2 graph, which uses a client library to communicate with other nodes. Nodes can communicate with other nodes within the same process, in a different process, or on a different machine. Nodes are typically the unit of computation in a ROS graph; each node should do one logical thing.
Nodes can publish to named topics to deliver data to other nodes, or subscribe to named topics to get data from other nodes. They can also act as a service client to have another node perform a computation on their behalf, or as a service server to provide functionality to other nodes.

## Slide 7: Technical Foundations
ROS2 Actions
Notes: Actions are one of the communication types in ROS 2 and are intended for long running tasks. They consist of three parts: a goal, feedback, and a result.
Actions are built on topics and services. Their functionality is like services, except actions are preemptable (you can cancel them while executing). They also provide steady feedback, as opposed to services which return a single response.
Actions use a client-server model, like the publisher-subscriber model. An “action client” node sends a goal to an “action server” node that acknowledges the goal and returns a stream of feedback and a result.

## Slide 8: Technical Foundations
ROS2 Robotics Workflow
Notes: ROS2 Layers :
App Layer : where the high level commands come ( RVIZ or some ros2 node )
3rd party software : like Movit2 for motion planning, manipulation, 3D perception, kinematics, control, and navigation.
Controllers

## Slide 9: System Architecture
Notes: System overview :

## Slide 10: System Architecture
TCP Connection to the Robot

## Slide 11: System Architecture
ROS2 Robot Description
URDF File
Robot Parts
Gazebo Parts
Ros Control

## Slide 12: System Architecture
ROS2 Control - Overview
Joint Trajectory Controller
Configuration Yaml File
Control Manager
Hardware Interface
Kuka KR3-R540
Send Points to Robot

## Slide 13: System Architecture
ROS2 Control – Joint Trajectory Controller (JTC)
JTC
Interpolation Spline ( linear)
Trajectory Point/s
( Joint Space !)
Joint Trajectory

## Slide 14: System Architecture
ROS2 Control – Joint Trajectory Controller (JTC) – example Interpolation Spline ( linear)

## Slide 15: System Architecture
ROS2 Kinematics
Inverse Kinematics Action Server
Using Levenberg-Marquardt Method (KDL Library)
Points in cartesian Space
Points in Joint Space

## Slide 16: System Architecture
ROS2 Kinematics - Example

## Slide 17: System Architecture
ROS2 Kinematics
Forward Kinematics – Publisher Node
Using recursive forward position kinematics algorithm
Joint Space Points
Cartesian Space points

## Slide 18: System Architecture
Path Planning Sequence
Sequence of Pose points in Cartesian Space
Interpolation in Cartesian space
Cartesian geometric path ( position and orientation )
Path sampling and inverse kinematic
Sequence of Pose points in Joint space
Using JTC to Interpolating them into a Trajectory
Geometric path in Joint space
Using PTP on Kuka to move the robot (only follows the point sent and dose not calculate new path )
Those steps are not implemented into the system , could be implemented in the future

## Slide 19: System Architecture
OPCUA Server

## Slide 20: System Architecture
GUI – OPCUA Client
Login and Register
Registering users with authentication functionalities
Docker Build and run
Building the system inside a docker image and run it
OPCUA Client
Starting the OPCUA Client and connecting it to the Server inside the image
Robot Control
Starting the Simulation and real robot and control the DT inside the docker image
MongoDB as Backend
System have a Mongo database as a backend

## Slide 21: System Architecture
GUI – OPCUA Client – Register

## Slide 22: System Architecture
GUI – OPCUA Client – Login

## Slide 23: System Architecture
GUI – OPCUA Client – Docker

## Slide 24: System Architecture
GUI – OPCUA Client – OPCUA Connection

## Slide 25: System Architecture
GUI – OPCUA Client – Dashboard

## Slide 26: System Architecture
Docker
Running inside the Docker Image
Builds the Docker Image and runs it

## Slide 27: System Workflow
Overview

## Slide 28: Use case – Visual Commission
Overview
User - Student
Dashboard - App
System – Simulation
System – real
Testing points, paths , creating Tasks ,testing collusion
Sending Feedback from Simulation
Sending Feedback from Real Robot
Running Paths on the real robot after choosing right configurations

## Slide 29: Areas for Improvement
As Mentioned, The Path planning is missing some steps to achieve a cartesian path planning sequence
The Simulation needs some improvements , as in adding the Cabinet of the robot and all the objects inside it to create a replica of the workstation.
The system also needs an implementation of a collusion detection algorithm to help with the robot movement.
The GUI and Database could be improved by adding :
  A workflow that gathers tasks together
  A display for all tasks stored in the database
  A better management of the Tasks inside of the database ( delete or update the Tasks are missing) , where we delete the entire Tasks of the user currently.
  Maybe moving the App from a Desktop to web app is a good approach.
Changes to the controller :
  Use Position and velocity interfaces so that we can use Cubic splines instead of linear ( smoother movement of the robot )
  Expanding the Hardware interface to support the velocity interface so that it can control the real robot joints velocity

## Slide 30: DEMO

## Slide 31: Vielen Dank für Ihre Aufmerksamkeit.
www.thu.de